## Slide 1: Computer Network

## Slide 2: Computer Network and the Internet
Chapter 1

## Slide 3: Internet
End System / Host: device connects to the Internet.
Communication Link & Packet Switch: connect hosts.
Packet: Network traffic segmentation.
Internet Standard: IETF-RFC.
API: Application Programming Interface.

## Slide 4: Network Core
Circuit switch & Packet switch.
Frequency-Division Multiplexing FDM
Statistical Multiplexing

## Slide 5: Delay
Delay = nodal processing delay + queuing delay + transmission delay + propagation delay
Packet loss: packet drop.

## Slide 6: Layer Model
Protocol stack: network layers. ISO-OSI
Application Layer: HTTP, SMTP
Transmission Layer: TCP, UDP
Network Layer: IP

## Slide 7: Layer Model

## Slide 8: Application Layer: HTTP & DNS
Chapter 2

## Slide 9: Application – Client and Server

## Slide 10: TCP & UDP
TCP:
  Reliable data transmission.
  Connection Oriented.
UDP:

## Slide 11: HTTP
Hyper Text Transfer Protocol, HTTP.
Web: objects / elements.
HTTP uses TCP.

## Slide 12: HTTP

## Slide 13: HTTP
Cookie: session control.

## Slide 14: FTP
FTP with 2 parallel TCP connection:
  Control connection
  Data connection

## Slide 15: DNS
Domain Name Service, DNS
  Host aliasing
  Load distribution
DNS cache: local storage DNS record.

## Slide 16: Transmission Layer: TCP & UDP
Chapter 3

## Slide 17: TCP & UDP
IP: unreliable, best-effort delivery service.
Transport layer multiplexing & demultiplexing.
Port: source port & destination port.

## Slide 18: UDP
Better control of data and transmission time.
No connection.
No connection state.
Segment header size small.

## Slide 19: UDP
UDP packet format:
Checksum: sum of data (16bits, backrush) and negative.

## Slide 20: TCP

## Slide 21: TCP

## Slide 22: Network Layer: IP
Chapter 4

## Slide 23: Forwarding, Routing
Forwarding: router chooses output link.
Routing: network layer decides path.
Network service model:
  Delivery confirm.
  Delivery with upper time bound.
  Orderly packet delivery.
  Minimal traffic width.
  Upper delay jitter.
  Security service.

## Slide 24: IPv4

## Slide 25: IPv4
IP packet length: smaller than 1500 bytes.
Checksum: similar to UDP checksum.
MTU: Maximum Transmission Unit.

## Slide 26: NAT
Network Address Translation, NAT

## Slide 27: IPv6
Basic headers & extension headers.

## Slide 28: Link Layer and LAN
Chapter 5

## Slide 29: Link-layer Protocol
Framing: package network layer packet to frame.
Link access: Media Access Control, MAC.
Reliable delivery: used in WiFi.
Flow control: buffer.
Error detection & Error correction.
Half-duplex and full-duplex.

## Slide 30: Link-layer
Main part of link layer is in network adapter.

## Slide 31: Even-odd Parity
Sum of all bits and even-odd check bit is even.
Two-dimensional parity:

## Slide 32: Reference
计算机网络：自顶向下方法
TCP/IP详解：卷一
Wireshark数据包分析实战